## Slide 1: State Project No. 0017-0196 Route 72 Improvements in the City of Bristol
DESGIN EXCEPTIONS MEETING
August 28, 2025
Prepared by: GM2 Associates, Inc.
Prepared for: City of Bristol

## Slide 2: Organizational Chart
GM2 Staff | Stakeholder Representatives | CTDOT Liaisons
Principal In Charge Matthew Vail | Raymond Rogozinski | Principal Engineer Michael Cherpak
Project Manager Paul Brand | Justin Malley | Supervising Engineer Devin Racicot
Project Engineer Danielle Dixon |  | Right of Way Coordinator Zachary Guarino
Project No. 0017-0196

## Slide 3: General Project Information
Project Origin
  Streetscape Study and Design Concepts completed in 2021
    Riverside Avenue
    Divinity Street
    Park Street
Purpose & Need
  Purpose: To improve safety, access management, pedestrian accommodations and aesthetic qualities along Riverside Avenue.
  Need: Current condition of existing facilities along Riverside Avenue and the poorly developed and disconnected sidewalk system.
Project No. 0017-0196

## Slide 4: General Project Information
Project Schedule
  Contract Documents: September 2026
  Advertising: December 2026
  Construction: April 2027
Project No. 0017-0196
Project Cost
  Total Construction Cost: $12,600,000
  Right of Way: $465,000
Funding
  Project Design
    City of Bristol
  Rights of Way, Construction Phase Cost
    CT Department of Transportation
    Department of Economic and Community Development – Community Investment Fund Grant

## Slide 5: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
DESIGN EXCPETIONS
Project No. 0017-0196

## Slide 6: Project Locations
Rockwell
Park
Memorial Blvd Park
West Cemetery
Bristol
Hospital
Project No. 0017-0196

## Slide 7: Projects Locations
72
72
69
Muzzy Field
Memorial
Blvd Park
0017-0193
0017-0192
L017-0002
0017-0187
0171-0504
0017-0195
PARK STREET
RIVERSIDE AVENUE
273 Riverside Ave Site Work
Carousel Museum Site Work
Project No. 0017-0196

## Slide 8: Project Location
Riverside Ave
Memorial Blvd.
Mellen St.
Hooker Ct.
East St.
Main Street
Blakeslee St.
Memorial Blvd Park
Project No. 0017-0196

## Slide 9: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
DESIGN EXCEPTIONS
Project No. 0017-0196

## Slide 10: Existing Conditions
Corridor Information
  Functional Classification
    Riverside Avenue: Urban Principal Arterial (Built-up)
    Local Roads: Urban Local Roads (Built-up)
  Average Daily Traffic Counts (ADT)
  Posted Speed Limits
Roadway | 2021 ADT (vpd)
Riverside Ave | 8,700
Main Street | 5,600
Roadway | Posted Speed Limit
Riverside Ave | 30 m.p.h.
Main Street | 25 m.p.h.
Mellen Street | 25 m.p.h.
East Street | 30 m.p.h.
Project No. 0017-0196

## Slide 11: Existing Conditions
Typical Section:
Project No. 0017-0196

## Slide 12: Existing Conditions
Wide Curb Cuts
Random Ingress and Egress
Low Aesthetic quality
No Formal Streetscape
Utility Poles on both sides of the street (some located in driveways)
Project No. 0017-0196

## Slide 13: Existing Conditions
Pedestrian Accommodations
  Disconnected and Poorly Developed
  Poor Condition
  Inconsistent and Infrequent Buffer
  Scarcity of ADA-Compliant Curb Ramps
Project No. 0017-0196

## Slide 14: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
DESIGN EXCEPCTIONS
Project No. 0017-0196

## Slide 15: Safety Analysis
Crash Type | Number of Crashes | Percentage
Front to Rear | 64 | 41.8
Angle | 42 | 27.5
Fixed Object | 26 | 17.0
Time of Day | Number of Crashes | Percentage
Daylight | 108 | 70.6
Dark-Lighted | 38 | 24.7
Crash Data
Crash Data Collected from Connecticut Crash Data Repository Traffic Safety Dashboard.
    2017 – 2019, 2022, 2023
Calculated Crash Rate and Critical Crash Rate for each roadway segment and intersection.
All observed Crash Rates are below the Critical Crash Rate.
5-Year Period
153 Crashes
0 Fatalities
2 Severe Injuries
N
Project No. 0017-0196

## Slide 16: Safety Analysis
Crash Type | Number of Crashes | Percentage
Front to Rear | 64 | 41.8
Angle | 42 | 27.5
Fixed Object | 26 | 17.0
What does this Mean?
Crashes are below the expected average levels for the corridor
The leading crash types are logical based of the density of driveways along the corridor
Why are we seeing Fixed Object Crashes as a common crash type?
Existing Streetscape
  Wide seas of pavement
  Poorly defined edge of Road
Project No. 0017-0196

## Slide 17: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
DESIGN EXCEPTIONS
Project No. 0017-0196

## Slide 18: Proposed Improvements
Full Depth Reconstruction
Granite Stone Curbing
Standardization of Driveways
3.5’ Brick Sidewalk
5’ Sidewalks
Decorative Lighting
Project No. 0017-0196
Pavement Structure
4” HMA S0.5
3” HMA S1.0
12” Subbase

## Slide 19
Project No. 0017-0196

## Slide 20
Project No. 0017-0196

## Slide 21
Project No. 0017-0196

## Slide 22
Project No. 0017-0196

## Slide 23: Proposed Improvements
347 Riverside Ave
N
Riverside Ave
337 Riverside Ave
N
Riverside Ave
331 Riverside Ave
Project No. 0017-0196

## Slide 24: Proposed Improvements
347 Riverside Ave
N
Riverside Ave
337 Riverside Ave
Project No. 0017-0196

## Slide 25: Proposed Improvements
331 Riverside Ave
337 Riverside Ave
347 Riverside Ave
Project No. 0017-0196

## Slide 26: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
DESIGN EXCETPIONS
Project No. 0017-0196

## Slide 27: Design Standards
Project No. 0017-0196
Design Element | Design Standard | Existing Conditions | Proposed Design
Travel Lane Width | 10’ – 12’ | 12’ | 11’
Shoulder Width | 4’ – 8’ | 4’ –6’ | 4’
Cross Slope Travel Lane | 1.5% - 2.0% | 1.5% | 2.0%
Cross Slope Shoulder | 4.0% - 6.0% | 5.0% | 4.0%
Minimum Radius | 375’ | 275’ | 400’
Max Grade | 11.0% | 3.98% | 4.25%
Stopping Sight Distance | 250’ | 406’ | 320’
Superelevation Rate | 4.0% | <4.0% | 2.4%
Intersection Sight Distance | 390’ | Varies | Varies*
Clear Zone | To ROW line | 8’ | 9’
*Requires Design Exception

## Slide 28: ISD Design Exceptions
Project No. 0017-0196
3 Intersections:
  Route 72 & Warner Court
      LT-Turn ISD: Matches Existing Condtion
  Route 72 & Mellen Street
      LT-Turn ISD: Improved from existing condition
      RT-Turn ISD: Improved from Existing Condtion
  Route 72 & East Street/Hooker Court
      Sightline Easements
56 Proposed Driveways:
  112 ISDs
  73 Substandard ISDs at Driveways

## Slide 29: Route 72 & Warner Court
Field photos
 | Turn Direction | Standard ISD (ft) | Design Speed | Existing ISD (ft) | Ex. ISD Speed (MPH) | Proposed ISD Speed (ft) | Proposed ISD Speed (MPH)
Warner Court | Left | 390 | 35 | 350 | 31 | 350 | 31

## Slide 32: Route 72 & Warner Court

## Slide 33: Route 72 & Mellen Street
Field photos
 | Turn Direction | Standard ISD (ft) | Design Speed | Existing ISD (ft) | Ex. ISD Speed (MPH) | Proposed ISD Speed (ft) | Proposed ISD Speed (MPH)
Mellen Street | Left | 390 | 35 | 56 | <20 | 69 | <20
 | Right | 390 | 35 | 77 | <20 | 136 | <20

## Slide 38: ISD Design Exceptions
Project No. 0017-0196

## Slide 39
Project No. 0017-0196
38 Driveway ISDs improved from existing conditions

## Slide 41
Project No. 0017-0196
ISD Design Exceptions
34 Driveway ISDs match existing conditions

## Slide 43: ISD Design Exceptions
1 intersection ISD value decreases from existing conditions
  220 Riverside Avenue

## Slide 44: 220 Riverside Avenue
Existing Driveway Configuration:
  2 Aprons – 33’ & 34’ wide
  16’ separation between them

## Slide 45: 220 Riverside Avenue
Proposed Driveway Configuration:
  2 Aprons – 20’ wide
  18’ from property line
  44’ separation between them

## Slide 47: Recommendations
Justification:
  Proposed Design
    Improves existing substandard geometry
    Standardizes roadway width
    Improves Access Management
    All ISD values match or are improved from existing condtion with exception of one location
    No adverse effects to businesses along the corridor
  Increased Impacts & cost
    Property Acquisitions & sightline easements
    Realignment of Route 72
    Adverse effect to businesses along the corridor
    Outside the scope of the project
Project No. 0017-0196
It is recommended that exceptions to design standards for ISDs be granted for this project

## Slide 48: Route 72 Corridor
Project No. 0017-0196

## Slide 49: Proposed Improvements
Project No. 0017-0196

## Slide 50: Proposed Improvements
Project No. 0017-0196

## Slide 51: Bicycle Facilities
Bicycle Facilities are not Proposed under Project 0017-0196
Bristol partnered with Naugatuck Valley Council of Governments to conduct a study of potential downtown routing options to provide a safe, continuous connection between Rockwell Park in the west to Downtown, continuing east to Route 229.
Pequabuck River Trail Project will provide bike and pedestrian access from Rockwell Park to Memorial Boulevard and from Memorial Boulevard to Middle Street Trail.
Project No. 0017-0196

## Slide 52
Project No. 0017-0196
Project No. 0017-0196