## Slide 1: State Project No. 0017-0196 Route 72 Improvements in the City of Bristol
PUBLIC INFORMATION MEETING
April 29, 2025
Prepared by: GM2 Associates, Inc.
Prepared for: City of Bristol

## Slide 2: Riverside Avenue Overview
MEET THE PROJECT TEAM
MEETING FORMAT
TITLE VI – CIVIL RIGHTS
PROJECT PRESENTATION
QUESTION AND ANSWER
Project No. 0017-0196

## Slide 3: Organizational Chart
GM2 Staff | Stakeholder Representatives | CTDOT Liaisons
Principal In Charge Matthew Vail | Raymond Rogozinski | Principal Engineer Michael Cherpak
Project Manager Paul Brand | Justin Malley | Supervising Engineer Devin Raciot
Project Engineer Danielle Dixon |  | Right of Way Coordinator Zachary Guarino

## Slide 4: Meeting Format
Recording:
  https://bristolct.portal.civicclerk.com/
Submit a Question or Comment
  Q&A Session
  Email: RaymondRogozinski@bristolct.gov
  Telephone: Raymond Rogozinski at (860) 584-6125
Comment Period
  Open through May 13, 2025
  Email or Telephone

## Slide 5: Title VI – Civil Rights

## Slide 6: General Project Information
Project Origin
  Streetscape Study and Design Concepts completed in 2021
    Riverside Avenue
    Divinity Street
    Park Street
Purpose & Need
  Purpose: To improve safety, access management, pedestrian accommodations and aesthetic qualities along Riverside Avenue.
  Need: Current condtion of existing facilities along Riverside Avenue and the poorly developed and disconnected sidewalk system.

## Slide 7: General Project Information
Project Schedule
  Contract Documents: July 2026
  Advertising: September 2026
  Construction: April 2026
Funding | 
City of Bristol Project Design | CT Department of Transportation Fund & Perform Rights of Way Construction Phase Cost

## Slide 8: Route 72 Corridor
Project No. 0017-0196

## Slide 9: Project Locations
Rockwell
Park
Memorial Blvd Park
West Cemetery
Bristol
Hospital
Project No. 0017-0196

## Slide 10: Projects Locations
72
72
69
Muzzy Field
Memorial
Blvd Park
0017-0193
0017-0192
L017-0002
0017-0187
0171-0504
0017-0195
PARK STREET
RIVERSIDE AVENUE
273 Riverside Ave Site Work
Carousel Museum Site Work
Project No. 0017-0196

## Slide 11: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
Project No. 0017-0196

## Slide 12: Project Location
Riverside Ave
Memorial Blvd.
Mellen St.
Hooker Ct.
East St.
Main Street
Blakeslee St.
Memorial Blvd Park
Project No. 0017-0196

## Slide 13: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
Project No. 0017-0196

## Slide 14: Existing Conditions
Corridor Information
  Functional Classification
    Riverside Avenue: Urban Principal Arterial (Built-up)
    Local Roads: Urban Local Roads (Built-up)
  Average Daily Traffic Counts (ADT)
  Posted Speed Limits
Roadway | 2021 ADT (vpd)
Riverside Ave | 8,700
Main Street | 5,600
Roadway | Posted Speed Limit
Riverside Ave | 30 m.p.h.
Main Street | 25 m.p.h.
Mellen Street | 25 m.p.h.
East Street | 30 m.p.h.
Project No. 0017-0196

## Slide 15: Existing Conditions
Typical Section:
Project No. 0017-0196

## Slide 16: Existing Conditions
Wide Curb Cuts
Random Ingress and Egress
Low Aesthetic quality
No Formal Streetscape
Utility Poles on both sides of the street (some located in driveways)
Project No. 0017-0196

## Slide 17: Existing Conditions
Pedestrian Accommodations
  Disconnected and Poorly Developed
  Poor Condition
  Inconsistent and Infrequent Buffer
  Scarcity of ADA-Compliant Curb Ramps
  Non-existent Pedestrian Lighting
Project No. 0017-0196

## Slide 18: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
Project No. 0017-0196

## Slide 19: Safety Analysis
Crash Type | Number of Crashes | Percentage
Front to Rear | 64 | 41.8
Angle | 42 | 27.5
Fixed Object | 26 | 17.0
Time of Day | Number of Crashes | Percentage
Daylight | 108 | 70.6
Dark-Lighted | 38 | 24.7
Crash Data
Crash Data Collected from Connecticut Crash Data Repository Traffic Safety Dashboard.
    2017 – 2019, 2022, 2023
Calculated Crash Rate and Critical Crash Rate for each roadway segment and intersection.
All observed Crash Rates are below the Critical Crash Rate.
5-Year Period
153 Crashes
0 Fatalities
2 Severe Injuries
N
Project No. 0017-0196

## Slide 20: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
Project No. 0017-0196

## Slide 21: Proposed Improvements
Full Depth Reconstruction
Granite Stone Curbing
Standardization of Driveways
3.5’ Brick Sidewalk
5’ Sidewalks
Decorative Lighting
Project No. 0017-0196
Pavement Structure
4” HMA S0.5
3” HMA S1.0
12” Subbase

## Slide 22: Proposed Improvements
Project No. 0017-0196

## Slide 23
Project No. 0017-0196

## Slide 24
Project No. 0017-0196

## Slide 25
Project No. 0017-0196

## Slide 27: Proposed Improvements
347 Riverside Ave
N
Riverside Ave
337 Riverside Ave
N
Riverside Ave
331 Riverside Ave
Project No. 0017-0196

## Slide 28: Proposed Improvements
331 Riverside Ave
337 Riverside Ave
347 Riverside Ave
Project No. 0017-0196

## Slide 29: Proposed Improvements
370 Riverside Ave
N
370 Riverside Ave
Project No. 0017-0196

## Slide 30: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
Project No. 0017-0196

## Slide 31: Construction Staging
Project No. 0017-0196
Option 1: Daytime Work
  Maintain two-lanes of traffic
  Driveway access maintained
  Sidewalk access maintained
    Pedestrian Detours
Option 2: Nighttime Work
  Alternating one-way traffic
  Sidewalk access maintained
    Pedestrian Detours
  Final Paving

## Slide 32: Construction Staging
Project No. 0017-0196

## Slide 33: Construction Staging
Project No. 0017-0196

## Slide 34: Construction Staging
Riverside Ave
Mellen St.
Hooker Ct.
East St.
Project No. 0017-0196
Sidewalk Closed
Sidewalk Closed
Temporary Crosswalk

## Slide 35: Presentation Overview
PROJECT LOCATION
EXISTING CONDITIONS
SAFETY ANALYSIS
PROPOSED IMPROVEMENTS
CONSTRUCTION STAGING
OTHER CONSIDERATIONS
  Right Of Way
  Bicycle Facilities
  Design Exceptions
  Utilities
Project No. 0017-0196

## Slide 36: Right Of Way
  Function
    Acquire all property/property rights necessary for the project.
  Statutory References
    State of Connecticut: C.G.S. Section 13a-73 & 13a-98e
    Federal: Uniform Relocation Assistance and Real Property Acquisition Policies Act of 1970, as Amended.
  Impacts to Private Property*
    Partial Acquisitions
    Easements
    Rights
    *Impacts Subject to Change as Design Progresses
Project No. 0017-0196
Notes: 15 – Defined Easement for Highway Purposes
1 – Easement to install and Maintain end anchorage
1 – Partial Take

## Slide 37: Right Of Way
  ROW Process
    Letter of Intent to Acquire
    Valuation
    Offer of Compensation
    Negotiation
    Acquisition
      Agreement
      Condemnation
Project No. 0017-0196
Notes: 15 – Defined Easement for Highway Purposes
1 – Easement to install and Maintain end anchorage
1 – Partial Take

## Slide 38: Right Of Way
Project No. 0017-0196
Rights | Number of Properties Impacted
Grade | 1
Construct Driveway | 38
Construct Parking Area | 2
Install Bituminous Concrete Curb | 1
Construct Retaining Wall | 2
Construct Sidewalk / Concrete Walk | 5
Remove and Reset Chain Link Fence | 1
Various Rights to install Drainage Items | 3
Easements | 
Install and Maintain End Anchorage | 1
Defined Easement for Highway Purposes (Sidewalk) | 15
Acquisition | 1
Notes: 15 – Defined Easement for Highway Purposes
1 – Easement to install and Maintain end anchorage
1 – Partial Take

## Slide 39: Bicycle Facilities
Bicycle Facilities are not Proposed under Project 0017-0196
Bristol partnered with Naugatuck Valley Council of Governments to conduct a study of potential downtown routing options to provide a safe, continuous connection between Rockwell Park in the west to Downtown, continuing east to Route 229.
Pequabuck River Trail Project will provide bike and pedestrian access from Rockwell Park to Memorial Boulevard and from Memorial Boulevard to Middle Street Trail.
Project No. 0017-0196

## Slide 40
Project No. 0017-0196
Project No. 0017-0196

## Slide 41: Design Exceptions
Project No. 0017-0196
Design Element | Design Standard | Proposed Design
Travel Lane Width | 10’ – 12’ | 11’
Shoulder Width | 4’ – 8’ | 4’
Typical Cross Slope Travel Lane Shoulder | 1.5% - 2.0% 4.0% - 6.0% | 1.5% 4.0%
Turn Lane | 1’ Less than TL Width – TL Width | 10’
Sidewalk Width | 5’ Minimum | 5’
Stopping Sight Distance | 250’ | 432’
Minimum Radius | 375’ | 400’
Superelevation Rate | 4.0% | 2.4%
Maximum Grade | 11.0% | 3.96%

## Slide 42: Design Exceptions
Anticipated Design Exceptions
  Intersection Sight Distance
Project No. 0017-0196

## Slide 43: Intersection Sight Distance
Project No. 0017-0196

## Slide 44
Project No. 0017-0196

## Slide 45: Intersection Sight Distance
Project No. 0017-0196

## Slide 46: Utilities
Utility companies with facilities in the project area:
  Eversource Energy – Electric Distribution
  Eversource Energy – Gas
  City of Bristol Water and Sewer Department
  Frontier Communications
  Comcast Cable
  Crown Castle
Project No. 0017-0196

## Slide 47: Utility Relocations
Project No. 0017-0196

## Slide 48: Utility Relocations
Project No. 0017-0196

## Slide 49: Summary
Purpose
  Purpose: To improve safety, access management, pedestrian accommodations and aesthetic qualities along Riverside Avenue.
Proposed Improvements
  Full Depth Reconstruction
  Granite Stone Curbing
  Standardization of Driveways
  3.5’ Brick Sidewalk
  5’ Sidewalks
  Decorative Lighting
Project Schedule
  Contract Documents: July 2026
  Advertising: September 2026
  Construction: April 2026
Project No. 0017-0196

## Slide 50: Questions and Answer
Recording:
  https://bristolct.portal.civicclerk.com/
Submit a Question or Comment
  Q&A Session
  Email: RaymondRogozinski@bristolct.gov
  Telephone: Raymond Rogozinski at (860) 584-6125
Comment Period is open through May 13, 2025, via Email or Telephone
Project No. 0017-0196